## Slide 1: Symbology Progress Update
Yanlai Wu
Advisor: Dr. Tang

## Slide 3: Visual Understanding Module

## Slide 4: Visual Understanding Module with Multi-Modal LLM
Core Function: The Visual Understanding module serves as an intelligent co-pilot, converting raw cockpit visual data (including charts, radar, and instruments) into concise semantic briefings.
LLM Integration: The VisionLLMClient interfaces with OpenAI-compatible APIs, supporting custom hosted models like Qwen/Qwen3-VL-32B-Instruct-FP8.
Real-time Feedback: Server-Sent Events (SSE) are handled to provide real-time feedback during long analysis generations.
Specialized Analysis: Implementations include the SectionalChartAnalyzer (identifying airspace frequencies and obstacle heights) and the WeatherRadarAnalyzer (mapping visual colors to meteorological severity, such as Light, Moderate, or Extreme Precipitation).
Qwen3-VL Model Pipeline

## Slide 5: Visual Understanding Module with Multi-Modal LLM

## Slide 6: Multi-Modal LLM visual capabilities
Accurately identifies and localizes HUD instruments in complex, dynamic scenes
Demonstrates pixel-level understanding and robust spatial reasoning

## Slide 7: Multi-Modal LLM visual capabilities

## Slide 8: Message Communication

## Slide 9: Message Communication
Executed on local machine running LLM or other stuff (w/o public IP)
Local Machine (w/o public IP)
Remote Machine (with public IP)
Nginx Proxy Pass
Local Devices
LLM on local machine
https://game.agaii.org/mllm
SSH reverse tunnel

## Slide 10: Traffic Radar Module

## Slide 11: Traffic Radar Module
Overview and Purpose
• Function: A complete TCAS-like (Traffic Collision Avoidance System) display powered by live ADS-B data.
• Data Handling: The TrafficRadarDataManager implements a rigorous caching strategy, requesting data from the Airplanes.live API only when the aircraft moves significantly or a time threshold expires.
• Priority Sorting: Targets are sorted so the most dangerous ones are processed and displayed first if system limits are hit.
Display Features
• Rendering: Uses a mask component to clip the display to a circle.
• Visualization Modes: Supports Track-Up Mode, which rotates the display and compass rose based on the aircraft heading.
• Underlays: Integrates with a provider to render Sectional Chart map tiles beneath the radar targets, maintaining correct rotation and scale.
• User Experience: Employs Micro-Animations to smoothly interpolate range changes (e.g., zooming from 10nm to 20nm) to prevent jarring visual jumps.

## Slide 12: Weather 2D/3D Module

## Slide 13: Weather 2D Module
• Composite Radar System: Fetches, stitches, and processes real-world weather data.
• Tile Architecture: The NOAAWeatherProvider acts as a mapping engine, dynamically selecting API zoom levels (1-10) based on the radar's generic range setting (NM).
• Compositing Strategy: Downloads a grid of 256px tiles (e.g., 3x3 or 5x5) and blits them into a single large Texture2D composite.
• Virtual Camera: The final "Radar Texture" uses a virtual camera that pans and rotates over the static composite to match the aircraft heading, preventing data re-download when the plane turns.

## Slide 14: Weather 3D Module- under experimenting

## Slide 15: Future visualization plan for 3D weather

## Slide 16: Voice Control System

## Slide 17: Voice Control

## Slide 18: Voice Control Logic

## Slide 19: Indicator System Update

## Slide 20: Indicator Module
Core Function & Architecture
• System Purpose: Functions as a screen-space Augmented Reality (AR) overlay system. It visualizes targets, including Traffic, Waypoints, and Hazards, even when these objects are outside the camera view.
• Proximity Logic: The system implements dynamic opacity rules, allowing it to fade out distant targets or make high-priority threats pulse.
Advanced Rendering Features
• Dual Visualization: The IndicatorElement switches between displaying a "Symbol" when the target is on-screen and an "Arrow" when the target is off-screen.
• Pseudo-3D Effect: It creates a "pseudo-3D" effect by rotating the 2D UI symbol to match the target's pitch and bank.
• Navigation Lights: The module procedurally generates navigation lights—Port (Red), Starboard (Green), and Tail (White)—for traffic targets based on the viewer's relative position.

## Slide 21
DEMO